## Slide 1
HANSI ZOE
AI GOGGLES
DIY AI-Powered Smart Goggles with ESP32-S3
Inspired by Hange Zoe from Attack on Titan
Sola | TH Nurnberg (B-AMP) | AlgoSphere Quant | ExMachina Labs | 2026

## Slide 2
THE VISION
THE PROBLEM
Smartphones break immersion
AR glasses cost $300-1500+
No open-source DIY option
Existing wearables lack AI integration
THE SOLUTION
DIY goggles for ~150 EUR total
AI vision, translation, voice assistant
HUD prism display in field of view
Open-source, hackable, extensible
Goal: Build AI-powered smart goggles that combine computer vision, NLP, and AR — for under 200 EUR.

## Slide 3
SYSTEM ARCHITECTURE
GOGGLES LAYER
ESP32-S3 @ 240MHz
OV2640 Camera (VGA)
PDM Microphone 16kHz
NimBLE GATT Server
VAD + Ring Buffer
Deep Sleep: 14uA
COMPANION APP
Web Bluetooth API
Whisper STT Pipeline
AI Router (multi-provider)
TTS Engine
RAG Memory (256d vectors)
HUD Compositor
AI CLOUD
GPT-4o Vision + Mini
Claude Sonnet 4
Groq Llama 3.3 (free)
OpenAI Embeddings
Whisper Transcription
OpenAI TTS Nova
BLE
API

## Slide 4
FIVE AI MODES
SCOUT
Real-time object & text identification via GPT-4o Vision. OCR, technical component ID, navigation.
BABEL
Instant translation: 12+ languages. OCR image text, voice translation, manual input. Auto TTS output.
TITAN
Voice conversational AI with RAG memory. Recalls past observations. Push-to-talk or hands-free.
SURVEY
Life-logging camera. Auto-captures and AI-describes scenes every 10s. Searchable memory archive.
COMBAT
Navigation mode with GPS waypoints, landmark detection, and spatial audio cues on the HUD.

## Slide 5
HARDWARE
Component | Model | Cost
Base Frame | Uvex Flex Seal OTG Goggles | 15 EUR
Compute | Seeed XIAO ESP32-S3 Sense | 14 EUR
HUD Display | LILYGO T-Glass V2 (126x126 AMOLED + Prism) | 48 EUR
Battery | LiPo 3.7V 600-1000mAh | 5-8 EUR
Audio | INMP441 Mic + MAX98357A Amp | 7 EUR
Sensors | BME280 + WS2812B LEDs | 5 EUR
Wiring | Silicone wires, JST, PCB proto | 10 EUR
3D Print | PLA/PETG filament (FabLab) | 8 EUR
TOTAL: ~150-200 EUR

## Slide 6
VOICE PIPELINE
MIC
PDM 16kHz
on ESP32-S3
VAD
Energy-based
detection
BLE
WAV chunks
to phone
STT
Whisper API
transcription
LLM
GPT-4o / Claude
+ RAG context
TTS
Browser Speech
or OpenAI Nova
HUD
Text relay
to T-Glass
End-to-end latency: ~2-4 seconds | Push-to-Talk + Hands-Free VAD | 3 voice modes
RAG MEMORY SYSTEM
Every observation stored as 256-dim embedding
Cosine similarity search for relevant context
Top-5 memories injected into LLM prompt (RAG)
"What did I see earlier?" queries work across sessions

## Slide 7
TECH STACK
FIRMWARE
C/C++, Arduino/ESP-IDF, NimBLE, LVGL, FreeRTOS, I2S PDM, ESP-Camera
COMPANION APP
HTML5/JS, Web Bluetooth API, Web Audio, Web Speech API, IndexedDB, Canvas
AI / ML
GPT-4o Vision, Claude Sonnet, Groq Llama 3.3, Whisper STT, OpenAI Embeddings, TTS
HARDWARE
ESP32-S3, OV2640, LILYGO T-Glass V2, AMOLED+Prism, BLE 5.0, LiPo power
TOOLS
PlatformIO, VS Code, FreeCAD, KiCad, Git/GitHub, Chrome DevTools

## Slide 8
PHYSICAL DESIGN
Hansi Zoe Aesthetic — Attack on Titan Inspired
BASE FRAME
Uvex Flex Seal OTG safety goggles. Fits over prescription glasses. Matte black spray paint finish. Leather strap replacement for steampunk aesthetic.
ELECTRONICS MOUNT
3D printed (PETG) bracket on right temple. Houses XIAO ESP32-S3 + battery. Snap-fit design for easy removal. Cable routing channels.
HUD PRISM
T-Glass V2 mounted on right temple arm, angled 15 deg inward. Prism projects 126x126 image into upper-right FOV. Adjustable angle bracket.
FINISHING
Amber-tinted LED accents (WS2812B). Brass rivets and buckles. Weathered leather straps. Engraved "ExMachina" logo.

## Slide 9
KEY METRICS
~150 EUR
Total Build Cost
2-4s
AI Response Latency
3-4h
Active Battery Life
5
AI Operation Modes
12+
Translation Languages
256d
RAG Memory Vectors

## Slide 10
THANK YOU
Open-source AI wearable built with passion, curiosity, and code.
GitHub: github.com/[your-repo]/hansi-ai-goggles
Built by Sola — TH Nurnberg B-AMP Program
AlgoSphere Quant | ExMachina Labs
"If you don't try, you'll never know." — Hange Zoe